## Slide 1
Vortex Flow Control
Optimizing Storage Efficiency
Underground Stormwater Storage and Treatment Workshop
Phillip Taylor
Stormwater Solutions Specialist
Hydro International
03/04/2014

## Slide 2
Sizing Assumption
Site size 1 ac
Pre-development C = 0.34
Post Development C = 0.99
Rational Method
1” Rainfall
60 minute duration

## Slide 3
Pre-Development Condition
C = 0.34
Runoff Rate = 0.34 cfs

## Slide 4
Post Development Condition
C = 0.99
Runoff Rate = 1.0 cfs

## Slide 5
Outlet Control Condition
Must Attenuate 1 cfs inflow to 0.34 cfs outflow

## Slide 6
Require Underground Storage

## Slide 7
Three-inch Orifice Flow Control

## Slide 8
Size SC-310 Chamber Field (3” Outlet)
0.066 af / 0.084 af = 79% Efficient
Max Release Allow: 0.34 cfs

## Slide 9
Re-size SC-310 for Efficiency (3” Outlet)
0.065 af / 0.068 af = 96% Efficient

## Slide 10: Construction Summary
SC-310 Chambers sized for max efficiency
 | Quantity (Labor) | Stone (cy.) | Excavation (cy.) | Footprint (sq.ft.)
SC-310 + 3-in Orifice | 90 | 151 | 201 | 2326

## Slide 11
Deeper Storage SC-740 Chambers

## Slide 12
SC 740 with 2.8” Outlet
0.064 af / 0.074 af = 87% Efficient

## Slide 13
Construction Savings
 | Quantity (Labor) | Stone (cy.) | Excavation (cy.) | Footprint (sq.ft.)
SC-310 + 3-in Orifice | 90 | 151 | 201 | 2326
SC-740 + 2.8-in Orifice | 40 | 126 | 195 | 1502
Savings | 55% | 17% | 3% | 35%

## Slide 14
Hydro 5” Reg-U-Flo Valve
“S” Type
“C” Type
Flow control for stormwater detention
Catch basin inlet flow control
Erosion control and energy dissipation
Aeration of stormwater storage discharges
Pre-development hydrograph matching
Notes: Purpose of Slide:
To explain the valve types.
Key Points:
“S” Type or snail shell type are used where a wet sump is wanted but can be mounted both horizontally or vertically.
“C” Type are flush invert and are used mainly in dry basin or flood control situations.
Information:

## Slide 15
Different Discharge Curve
Head (ft)
Flow (cfs)

## Slide 16
5-inch RUF Valve and SC-740
100% Efficient!

## Slide 17
Construction Savings
 | Quantity (Labor) | Stone (cy.) | Excavation (cy.) | Footprint (sq.ft.)
SC-310 + 3-in Orifice | 90 | 151 | 201 | 2326
SC-740 + 2.8-in Orifice | 40 | 126 | 195 | 1502
Savings | 55% | 17% | 3% | 35%
SC-740 + 5-in Vortex | 32 | 103 | 158 | 1221
Savings | 20% | 18% | 19% | 19%

## Slide 18: Reg-U-Flo® Optimum
Flush FloTM
Kick-Flo®
Head
Flow